JOB HAZARD ANALYSIS - Task Specific

Workplace Task to be analyzed:	 Use and maintenance of Electrical Lab Equipment

Department:

McMaster Job Title:

McMaster Hazard Category:	Physical/Energy

Hazard Type:  Electric shock / fire

JCQ# (if applicable):

Loss Potential Rating (please circle):MAJOR     MODERATE     MINOR

*If rated as MAJOR a Standard Operating Procedure (SOP) is mandatory

Required Personal Protective Equipment (please circle): Head Hearing Breathing Eye Hand Foot Knee Full Body

| Sequence of Task | Potential Hazards | Action or Procedure | Required Training |
| --- | --- | --- | --- |
| Read all SOP’s or manuals associated with the equipment |  |  | WHMIS Work place specific |
| Plugging in equipment | Electric shock Blown fuse – spark or flame can occur at outlet Running cable across floor can cause a tripping hazard | Plugs that are cracked or broken must not be used and cables must be in good condition The rating of the fuse must be appropriate to the appliance. Cables must not be run across the floor in such a way as to cause a tripping hazard or to be susceptible to damage from passing traffic. If it is necessary to run cables across walkways, they must be covered with cable protectors. |  |
| Use of equipment | Electrical equipment is a possible source of ignition. Presence of water can cause an electrical short ciruit with sparks/flames or cause electrocution | Electrical equipment must not be used in the vicinity of flammable or explosive gases Electrical equipment must not be used where it may get wet - Equipment that has been wet must never be switched on until the equipment has been tested. Anyone to whom the equipment is taken for testing must be informed about what has happened. |  |

# Text boxes

*Supervisor needs to review with worker and both signatures are required below

Date: ___________________________________

Reviewed by Supervisor: ___________________

Employee Signature: _______________________

Supervisor Signature: ______________________